## Slide 1
Republic of Turkey
Ministry of Forestry and Water Works
Turkish State Meteorological Service
Black Sea and Middle East Flash Flood Guidance System
Yusuf ULUPINAR
Turkish State Meteorological Service
yulupinar@mgm.gov.tr

## Slide 2
Objectives
Climate change has caused an increase in the number of severe weather events in many countries, and it has led to an increase in violence.
85% and 15% of the floods are characterized as flash floods and river floods, respectively.
Flash floods cause more than 5000 fatalities per year all over the world.

## Slide 3
Objectives
to provide real time flash flood warnings with high hit rate,
to reduce the loss of life and property damages that may occur in the flash flood prone areas all over the world.

## Slide 4
Black Sea and Middle East
Flash Flood Guidance System
In 2007, WMO decided to establish 22 Regional Centers worldwide, and it has created 7 regional centers by now.
The initial meeting of Black Sea and Middle East Flash Flood Guidance System was held in İstanbul on 29-31 March 2010, and Turkey has been elected as the regional center.

## Slide 5
Flash Flood Guidance Model Concept

## Slide 6
Land Cover
Land Cover
Source: Republic of Turkey Ministry of Forestry and Water Works
1/100.000
Scale: 1/100.000
“Corine” land classification
5 basic classes; agricultural areas, forests, wetlands, artificial zones and water bodies are given.

## Slide 7
Source: USGS http://srtm.csi.cgiar.org
Topography
90 meters resolution DEM (Digital elevation Model) data from USGS has been applied. When the model has been obtained for Turkey, the model parameters have been improved to 30 meter resolution data.

## Slide 8
Soil Classification
Soil Data
Source: REPUBLIC OF TURKEY MINISTRY OF FOOD, AGRICULTURE AND LIVESTOCK
1/25.000
Prepared based on the USDA soil classification
There are 26 different soil groups in Turkey, e.g., alluvial soil, beach sand, brown soil etc.
Scale: 1/25.000

## Slide 9
Hydrological Parameters
The data for rivers, dams, ponds, and gauging stations are obtained from the State Hydraulic Works to use as inputs in the system.
There are 1478 State Hydraulic Works stations in Turkey.
19 station data, where flash flood events occurred in the past, are applied for the model calibration.
Source: DSİ
Scale: 1/250.000
Scale: 1/250.000
Dams and Ponds
Rivers
State Hydrolic Work Stations

## Slide 10
30 Year Historical Meteorological Data
Source: TSMS
Rain,
Temparature,
Sunshine duration,
Evaporation,
Soil moisture,
Wind.
Meteorological Parameters
30-year historical data are used to calibrate the model and determine the parameters.

## Slide 11
The formation of Sub-basin
More than 11.000 sub-basins with high resolution delineation for Turkey (current).
At the regional level, more than 16.800 sub-basins with an average area of 200 km were generated .
For Turkey, 2.900 sub-basins were generated (before).

## Slide 12
Radar
Precipitation
Infrared
Satellite
Persistent
Flash
Flood
Threat
Microvawe
Satellite
Surface
Observation
Merged Precipitation
Soil
Moisture
FFG
Imminent
Flash
Flood
Threat
Surface Observation Data
Main Product Console

## Slide 13
Surface Observation
The number of automatic meteorology observation station has increased to 850 from 138 because of the importance of hydrological studies, thereby the model has operated more accurate. Measured precipitation, temperature, snow, and evaporation data are entered into the model in real time.

## Slide 14
Radar Precipitation Data
After the bug fixes, hourly precipitation data obtained from 10 radars of TSMS are entered into the model with 450 x 720 m grid resolution. Radar precipitation products are updated in every 6 minutes.

## Slide 15
Satellite Precipitation Data
Global Hydro Estimator (GHE) is generated by NOAA-NESDIS by using IR window channels of NOAA and EUMETSAT geostationary satellites.
Microwave bias adjusted Global Hydro Estimator (MWGHE) is generated by NOAA-NESDIS by adjusting GHE precipitation with microwave precipitation retrievals from polar orbiting satellites.

## Slide 16
1.500 m
3.000 m
5.000 m
10.000 m
15.000 m
Infrared (10.5 µm)
Microwave
Precipitation data are calculated by using infrared sensors based on cloud-top height.
Microwave precipitation data are calculated by using the radiation that coming inside of the cloud.
Therefore, the microwave precipitation data are more accurate.
Tb
Satellite Precipitation Data
Tb

## Slide 17
Surface Observations
The measured areal precipitation data are entered into the model in real time and shown at the sub-basin scale.

## Slide 18
Merged Satellite Data
This product is derived for each basin based on the best available mean areal precipitation estimates from bias-adjusted RADAR or bias-adjusted MWGHE or bias-adjusted GHE or the gauge-interpolations. The Merged MAP data products are updated every hour and reflect accumulations of basin-average precipitation of a given duration ending on the current navigation hour.

## Slide 19
Soil moisture, run-off and infiltration products are generated by using the Sacramento SAC-SMA model.
Soil Moisture Model (SAC-SMA)

## Slide 20
Average Soil Moisture (ASM) product shows the fraction of soil moisture deficit of the upper soil (20-30 cm) for which upper zone tension and free water contents are estimated by using Sacramento Soil Moisture Accounting Model (SC-SMA).
Soil Moisture Model (SAC-SMA) Outputs

## Slide 21
h=Water Level
FFT (Flash Flood Threat)= excessive precipitation after filled creek channel (precipitation-FFG) (mm).
FFG= rainfall needed to fill creek channel (mm).
Surface Runoff and Infiltration
Flow (Q) Account in the outlet of sub-basin
Surface Runoff Threshold Model

## Slide 22
Surface Runoff Threshold Model
Soil water holding capacity and runoff are calculated based on precipitation and soil types by the Sacramento Soil Moisture Model.
FFG products are generated by the soil moisture and surface runoff data (Banket Level ve Sacramento Model).

## Slide 23
Flash Flood Guidance Model (FFG)
Flash Flood Guidance is defined as the amount of actual rainfall that causes bankfull flow at the end of the catchment for a given duration, e.g., 1-, 3-, and 6- hour. The main inputs of the FFG model are threshold runoff which is calculated with the geomorphologic unit hydrograph, drainage channel and catchment characteristics, and soil moisture deficit that is estimated from SAC-SMA model.

## Slide 24
Snow Products
Mean
Areal
Temperature
Snow
Cover
Area
Snow-Water Equivalent
Snow
Melt

## Slide 25
Temperature
Gauge mean areal temperature (GMAT) is generated by the synoptic observations that are disseminated through WMO Global Telecommunication System (GTS).

## Slide 26
Snow Cover Areas
24-hour snow cover area map is obtained from the satellite.

## Slide 27
Structure of the Snow Model
SNOW-17 model gets two parameters which are GMAT and merged MAP, and it produces a number of products including SWE and MELT by the thermodynamic equations.
Precipitation and Temperature
Snowpack
Energy change between Snow-Atmosphere
Rain and Melting
Snow Melt
Snow Cover Area
Transmission of excess water
Ground Melt
Water
Storage
Rain or Snow?
Energy
Deficit
Deficit=0.0
Rain
Y
K

## Slide 28
Snow Water Equivalent product is the direct output of SNOW-17 accumulation and estimated at 00, 06,12 and 18 UTC.
Snow Model Output

## Slide 29
The amount of snow melt products is obtained for 1 and 4 days for each sub-basin.
Snow Model Output

## Slide 30
ALARO Numerical Forecast Model was the only model used in the project until this time. However, BSMEFFG system started to use 3 different numerical models as ALARO, WRF and ECMWF since 18th August 2016.
Forecast Products
ALARO
Model
Output
ALARO
Forecast
Mean Areal Pre.
ALARO
Forecast
Flash Flood Threat
ECMWF
Model
Output
ECMWF
Forecast
Mean Areal Pre.
ECMWF
Forecast
Flash Flood Threat
WRF
Model
Output
WRF
Forecast
Mean Areal Pre.
WRF
Forecast
Flash Flood Threat

## Slide 31
ALADIN was the only numerical forecast model which has the highest resolution used in our country. Precipitation products that are updated in every 6 hours with 4.5 x 4.5 km resolution are entered into the model.
Numerical Weather Prediction Models

## Slide 32
Generated forecast precipitation products by using ALARO, ECMWF and WRF Numerical Weather Prediction Models are demonstrated in the figures, respectively.
Numerical Weather Prediction Models

## Slide 33
1-, 3-, 6-, and 24-hour accumulations of mean areal precipitation (mm) for each sub-basin are produced by using the numerical forecasts from the ALADIN, ECMWF and WRF models.
Forecast Mean Areal Precipitation

## Slide 34
Generated areal forecast precipitation products by using ALARO, ECMWF and WRF Numerical Weather Prediction Models are illustrated in the figures, respectively.
Forecast Mean Areal Precipitation

## Slide 35
FFT is the difference between forecast mean areal precipitation (FMAP) and FFG, and it is created at the model runtimes of 00, 06, 12 and 18 UTC. 1-hour, 3-hour, and 6-hour FFFTs are estimated at the model runtimes.
FFFT (06 UTC) = FMAP (06 UTC) - FFG (06 UTC)
Forecast Flash Flood Threat

## Slide 36
Generated forecast flash flood threat products by using ALARO, ECMWF and WRF Numerical Weather Prediction Models are shown in the figures, respectively
Forecast Flash Flood Threat

## Slide 37
Flash flood risk areas bulletins are prepared 6 hours in advance with the purpose of verification by means of BSMEFFG when there is potential risk of flash flood.
Flash Flood Risk Areas Bulletin

## Slide 38
24-Hour Forecast Mean Areal
Precipitation (FMAP)
Forecast precipitation maps are prepared by using the FMAP data in the GIS software.

## Slide 39
Flash Flood Risk Areas
Early warning maps are prepared with the FFFT data in the GIS software.

## Slide 40
SNOW 17 SNOW COVERED AREAS
SNOW 17 SNOW WATER EQUIVALENT
SNOW-17 THE AMOUNT OF SNOW MELT MAP
SNOW-WATER POTENTİAL MAP (25 BASIN)
By the Flash Flood Guidance Model, snow water potential and snow melt maps are prepared at basin scale for 1 and 4 days. Furthermore, these bulletins are shared with affiliated institutions.
Snow Water Equivalent and Analysis Bulletin

## Slide 41
Verification
                Verification reports are performed periodically by using FFGS bulletins. For instance, 67 Flash Flood Warning Bulletins were prepared throughout 2014. Flash flood events occurred in the areas that early warning was given in the 57 bulletins while there were no any recorded incidents for the other 10 bulletins.
 | Flash Flood Obs.(TSMS, DSİ, Press) |  |  | 
BULLETINS 2014 |  | YES | NO | TOTAL
 | YES | 57 (a) | 10 (b) | 67
 | NO | 48 (c) (DSİ + TSMS+ Press) | 250 (d) | 298
 | TOTAL | 105 | 260 | 365

## Slide 42
Verification Methods
                TSMS Fevk Obs., DSİ Flood reports, and flash flood news from press are the verification sources for the reports.

## Slide 43
Flash Flood events compared with Flash Flood Bulletins in 2014
                F.F. Bulletins, State Hydraulic Works flood reports, TSMS fevk obs., and flash flood news from press are indicated with the colors of purple, yellow, green, and blue, respectively.

## Slide 44
Training and Documentations
55 forecasters from 15 regional forecasting offices were trained about BSMEFFG products and how to use them in daily forecasting. It was held in Ankara at WMO RTC on 30 October-1 November 2013.
BSMEFFG user guide has been prepared both in Turkish and English.

## Slide 45
Meeting and Workshops
BSMEFFG regional workshop was held in Alanya WMO RTC, Turkey on 3-5 December 2013. As well as Turkey, Bulgaria, Georgia, Azerbaijan and Armenia, HRC and WMO representatives also participated in the meeting.
FFG products and case studies were covered in the workshop.

## Slide 46
Training for the Regional Countries
Participants in the BSMEFFG Training at Armenian Hydrometeorological Service
Participants in the BSMEFFG Training at Azerbaijan Hydrometeorological Service
Participants in the BSMEFFG Training at Georgia Hydrometeorological Service
BSMEFFG forecasters training was held at the Armenian , Azerbaijan and Georgia Hydrometeorological Services on 19-23 May , 26-29 May, and 21-25 July 2014 respectively.

## Slide 47
Lebanon and Jordan Hydrometeorological Services were trained about BSMEFFG on May 16-27, 2016 in TSMS.
BSMEFFG forecasters training coordinated by WMO was held for 8 regional countries at the Georgia Hydrometeorological Service on 28-30 June 2016.
Training for the Regional Countries

## Slide 48
SEEFFG Project
SEEFFG initial meeting was held in Ankara on January 22-24, 2013. Bosnia Herzegovina, Romania, Serbia, Croatia, Montenegro, Moldova, Slovenia, Macedonia, and Albania representatives attended to the meeting. Turkey was elected as the regional center of the SEEFFG project during the meeting.

## Slide 49
CAFFG initial meeting was held in Ankara on May 5-7, 2015. As well as World Meteorological Organization (WMO), Hydrology Research Center (HRC) and TSMS representatives, Kazakhstan, Turkmenistan, Uzbekistan, Tajikistan, and Kyrgyzstan representatives also attended to the meeting. Kazakhstan was elected as the regional center of the CAFFG project in the meeting.
Central Asian Countries
Flash Flood Guidance Project

## Slide 50
BSMEFFG Project was ended on December 31st, 2015. However, studies still continue to enhance the project.
BSMEFFG Project

## Slide 51
The studies of GIS-based, two- and three-dimensional views of the Flash Flood model products will be performed.
Representation of the Model Products

## Slide 52
FOR DETAILED INFORMATION:
PLEASE CONTACT WITH
MR. YUSUF ULUPINAR (yulupinar@mgm.gov.tr)